## Slide 1: Skippy structural parts overview
1-4 feets (3 transverse bar for lamp)
5 & 7 back and front
6 & 8 left and right sides
9-11 camera arch
12-15 camera holder frame
16 camera plate
17 main plate
1
2
5
4
7
6
9
8
11
10
3
12-15
16
17

## Slide 2: Frame components
1-4 feet elements
5+7 sidewalls
6+8 front and back

## Slide 3: Front and back
Rails position and nuts

## Slide 4: Secondary carriage
When you buy a secondary carriage they come with an additional black plastic spacer for transport. Carefully pull it out and make sure you don’t loose any ball bearings.

## Slide 5: Secondary carriage
Carefully add the carriage onto the rail. Do not force! Make sure you don’t loose any ball bearing

## Slide 6: Rails
There should now be two carriages on each of the main rails

## Slide 7: Rails
Use 9 M3*8mm screws and 9 m3 nuts to fasten the rails to the frame component as shown in picture
Do not tighten strongly the height of the rails needs to be adjusted later on
Add 2 M5 nuts on each side in the top and 3rd. Groove.
Add another 7 M5 nuts in the bottom grove (see arrow. Groove not seen in picture) these will become important later
Add 2 M5 nut in each row of groves in the back
Do this for each side

## Slide 8: Frame
This is how all the frame part should fit together

## Slide 9: Corner
There should be 2 m5 nuts on each of the frame component where the metal corner will be screwed in
On the frame piece 5 add a m3 nut in the top rail

## Slide 10: Metal corners
Please note that there are two different kind of 90° fasteners: the metalic ones have small tabs that fit into the grooves of the aluminium profiles and the black are smooth

## Slide 11: Fastener
Use M5 *8mm and metallic fasteners on frame piece 5 and 7 as shown on picture
Only mount them but do not tighten the screws so that the fasteners can still move freely

## Slide 12: Assemble frame base
Use more M5*8mm screws to assemble frame as shown

## Slide 13: Assemble frame base
Once all elements of the frame are in place make sure the frame is flat and tighten the screws well

## Slide 14: Finished frame base
This is how the frame should look from the top
Note that is should be flat and sit well on the table
If not flat loosen the screws press down on the table and tighten the screws again

## Slide 15: Feets
Flip the frame over so that the rails are now at the bottom
Add the feets as shown and add all the required nuts
Note that the two highlighted nuts are M3 the rest are M5
Notice the M5 nuts in the bottom grove of the sidewalls (arrows) as well as the corresponding nuts in the feet

## Slide 16: Mount feets
Flip prepared feet over and fasten to base frame with black metal corners and M5*8mm screws
Distance from left should be 4cm,21cm,44cm and 80cm respectively for the feet
Add rubberized stickers to feet as required

## Slide 17: Inside Frame
Flip the frame over and this is how it should look from inside.
Insert 3d printed spacers between foot and rail for the first and last foot (arrow)
adjust rail height so that the rails rest on the spacer at the front and back and tighten
Do this for both rails

## Slide 18: Power supply
The power supply has 2 holes for mounting

## Slide 19: Power supply
Use 2 m3*6mm screws to secure the power supply

## Slide 20: Printed parts
This is where some of the printed parts go

## Slide 21: Printed parts
Secure the 3d printed holder for the power electronics and the Arduino with 4 M5*8mm screws each

## Slide 22: Prepare main axis
Insert/screw 2 m3*8mm screws as shown

## Slide 23: Prepare main axis
Add aluminium coupler and tighten inbus screw. Make sure one screw tightens down on the flatened end of the stepper shaft
Attach the stepper to the holder and tighten the M3 screws
Make sure the cable comes out sideways as depicted

## Slide 24: Mount main axis stepper
Make sure the holder is more or less centered (17.5 cm from border) and screw lightly down with two M5*8mm screws

## Slide 25: Prepare the electronics
Unpack Arduino shield and 3 driver stepper driver board

## Slide 26: Prepare the electronic
Depending on used stepper driver stick cooler on the driver board

## Slide 27: Prepare the electronic
Insert driver board into Arduino shield make sure the polarity is correct (compare writing on both boards)

## Slide 28: Prepare the electronic
Insert Arduino shield on Arduino and plug in plastic holder

## Slide 29: Prepare endswitches
Unpack 2 endswitches and prepare the corresponding printed parts

## Slide 30: Prepare endswitches
Often the pins are very long and needs to be trimmed down

## Slide 31: Prepare endswitches
Insert switches into printed parts
insert a M3*8mm screw into the part hole

## Slide 32: Mount endswitch
Insert endswitch into rail and tighten screw to fasten

## Slide 33: Mount endswitch
Wedge endswitch behind the rail and use a M3*8mm screw to tighten

## Slide 34: Prepare endswitch cable
Endswitch cable should be 1m long
Cut cable after 43cm from the white plug

## Slide 35: Prepare endswitch cable
Crimp the end of the cable and add dupont plug

## Slide 36: Prepare endswitch cable
Cut the dupont plug from the second cable
Use the short end of the first cable and solder it to second cable.
New combined cable should be aprox. 92cm long

## Slide 37: Install power cable
Cut a 48 cm piece of power cable and connect Arduino shield power directly to power supply
Plug in short endswitch cable into endswitch
Cable manage and needed with plastic holder

## Slide 38: Endswitch
Plug in short endswitch to X- position as shown

## Slide 39: Endswitch
Plug in long endswitch cable into endswitch
Cablemanage as needed

## Slide 40: Endswitch
Plug in long endswitch cable into X+ position as shown

## Slide 41: Prepare lamp
Open lamp with a screwdriver by gently pushing plastic flaps

## Slide 42: Prepare lamp
When opening it should look similar to the following

## Slide 43: Prepare lamp
Cut the copper sense cable and throw away

## Slide 44: Prepare lamp
Cut a 40cm piece of power cable and push it through the screw hole as shown

## Slide 45: Prepare lamp
Ignore the electronics and find the connection to the led strip
Solder wire directly to the strip be carefull about the polarity

## Slide 46: Prepare lamp
Carefully close lamp back up

## Slide 47: Prepare lamp
Add double sided tape or Velcro tape to the bottom of the lamp

## Slide 48: Prepare lamp
Glue lamp to the small middle foot

## Slide 49: Prepare lamp
Connect the lap power cable to the Arduino shield as shown

## Slide 50: Prepare mains power cable
Cut about 1m of mains power cable add local plug to one end

## Slide 51: Mains power
Connect mains power cable to power supply
Follow the markings on the power supply as well as your local mains color coding
In this picture browns=phase blue=neutral
Green/yellow =grounding

## Slide 52: Power converter
Solder power cable to power converter 30cm on the input and 10cm on the output

## Slide 53: Power converter
Insert power converter in plastic holder and connect input directly to the power supply

## Slide 54: Power converter
Crimp end of the output cable and add a dupont plug as shown
Cut a 25cm piece of green cable crimp both end and connect as shown

## Slide 55: Led control
Plug green cable into the second top pin on the aux-3 connector

## Slide 56: X-axis stepper cable
Measure 40 cm from servo cable and cut
Crimp and add new dupont plug

## Slide 57: X-axis stepper
Plug in the first stepper driver
With blue cable facing forward ( opposite of what's in the picture. Turning the plug will invert stepper direction)

## Slide 58: Prepare X-carriage
Mount two T8 nut (2*8 matching main leadscrew ) into the carriage and screw it slightly with M3*8mm screws

## Slide 59: Prepare X-carriage
Make sure the T8 leadscrews can rotate freely and tighten the screws ( adjust T8 nut if necessary)

## Slide 60: X-axis endmount
Use printed x axis mount and T8 shaft support as shown
Insert M5*35mm screws into the holes
Note that depending on tolerances (from both pieces) it might be necessary to insert an additional washer between the part to achieve optimal height

## Slide 61: X-axis
Insert X-axis into coupler as shown

## Slide 62: X-axis
On the other end insert T8 leadscrew into holder and bolt down the M5 screws
Tighten hex screws on both ends (shaft coupler and shaft support)

## Slide 63: Prepare arch
Prepare 600mm aluminium profile as follow
All nuts are M5
Add additional M5 nuts at the bottom in every groove (arrows)

## Slide 64: Prepare arch
Repeat steps similar to X-axis
Use M3*8mm screws to bolt steppers to plastic and M5*8mm screws to bold plastic to aluminium profile
Distance from start of profile to bottom of plastic 19cm

## Slide 65: Prepare arch
Add coupler to each stepper

## Slide 66: Prepare arch
Add appropriate reinforcement plastic part at the bottom of the stepper (L & R are mirrored and not identical)

## Slide 67: Prepare arch
Slide plastic slider on both edges of the profile you just prepared
Note the added dupont plug to make the arch fully removable (more details later)

## Slide 68: Prepare arch top
Prepare 350mm aluminium profile as shown with 4 metallic connectors (+M5 nuts and screws)

## Slide 69: Arch
Assemble arch with M5*8mm screws

## Slide 70: Arch
Fasten arch to base frame as shown with 4 M5*8mm screws
Arch should be 40 cm from starting edge ( electronic side)

## Slide 71: Cables
This is how the whole assembly should look so far
To avoid having too much cable everywhere cut to length (74 cm left servo 47cm right servo) and redo the plug similar to X-axis
To make it more modular consider cutting the cable at 23cm on both side (until bottom) and add a dupont connection make connector cable with dupont plugs on both sides 25 and 52 cm long
with this arrangement the arch can be unplugged at the base and removed if needed

## Slide 72: cables
Cable manage as necessary using plastic clips and zip ties
Plug in servo cable in second and third stepper driver (order does not matter)

## Slide 73: Metal angles
Screw metal angles into the rail carriages with 8 M3*8mm screws on each side

## Slide 74: Table
Add metal table and bolt down with appropriate screws (short screws on the outside long screws in the middle connecting to the x-axis)

## Slide 75: Prepare Camera assembly
Prepare all the required pieces as shown

## Slide 76: Assemble z axis
Use printed z axis holder (similar to depicted) with one bronze T8 nut and 4 M3*20mm screw and corresponding M3 lock nut
Do this once for each side

## Slide 77: Camera frame
Add 4 M5 nuts in a 90° angle (only one depicted in what will be the bottom but should be 2)
Do this 2 times

## Slide 78: Camera frame
Copy nut configuration
Note that the 5 inner nuts are M3 nuts
Do this 2 times

## Slide 79: Camera frame
Assemble with metallic connectors and M5*8mm screws as follow

## Slide 80: Camera frame
Mount rails to camera frame assembly similar to main frame (M3*8mm screws)
Add rails stopper to both ends of rail

## Slide 81: Camera frame
Camera frame with rails and railstops mounted

## Slide 82: Z-axis
Add z axis holder (similar to picture) and fasten to bottom of frame with 2 M5*8mm screws each

## Slide 83: Z-axis
Add 20cm T8 leadscrew

## Slide 84: Camera holder
Fasten the camera metal base to the camera frame carriage with 4 M3*8mm screws on each side

## Slide 85: Camera holder
Add camera knob on the side as depicted

## Slide 86: Camera holder
Use double sides tape or screws to fasten 3d printed holder onto metal base

## Slide 87: Z-axis
Prepare the end of the Z-axis very similar to end of X axis but with different spacer and M5*16mm screws

## Slide 88: Z-axis
Make sure T8 leadscrew sticks out about 3-4 cm and put the whole assembly into the arch steppers

## Slide 89: Z-axis
Add the end of the Z-axis on both side
Fasten hex screws then tilt the ends vigorously to match the aluminium profile grooves width and fasten down the screws

## Slide 90: Z-axis
Fasten hex screw on coupler as well

## Slide 91: Prepare LED ring
Insert objektiv filter into the printed diffusion ring
Push down with some force so as to wedge the ring in the printed part
Make sure the thread of the filter is on the upper part sicking out of the part (as shown)

## Slide 92: Prepare LED ring
Separate the outer two LED rings from the rest

## Slide 93: Prepare LED ring
Strip about 2cm of the wires and tin them
Use the green wire to bridge DO and DI (Digital Out of the first ring into Digital In of the second ring)
Cut of left of green wire
Solder red and white wired on 5v and GND respectively
Solder leftover green wire on DI
Crimp dupont on the other end of the wire after aprox 10 cm

## Slide 94: Prepare LED ring
Insert Led ring firmly into printed diffusion ring

## Slide 95: Adjust power
DO NOT connect the Led ring yet!!!!!
Plug in power supply
While powered adjust output voltage to 5v by turning the small screw

## Slide 96: Upload firmware
Connect Arduino to computer
In Arduino studio find the right port and flash firmware onto arduino

## Slide 97: Plug in LED cable
Make a 1m cable of the same wire that you used for the LED ring and add dupont plugs on both ends
connect cable to power module and led ring

## Slide 98: Test everything
Connect skippy to power and computer
Start control software
Make sure all axis work fine
Make sure the endstops light up when pressed and work to stop X-axis when pressed
Makes sure both lightsources work
lubricate X and Z axis well with oil or grease (NO WD40!! WD40 is not a lubricant it’s a rust remover and will over time damage the leadscrews and nuts)

## Slide 99: DONE!
Congrats your successfully finished your skippy!!